## Slide 1: Influences of Magnetic Field Parameters on ECRIS Plasma Characteristics
The 24th International Workshop on ECR Ion Source
East Lansing, USA, September 28th, 2020
J. Li1
L. X. Li1,2, B. S. Bhaskar3,4, V. Toivanen3, O. Tarvainen3,5, D. Hitz1, L. B. Li1, W. Lu1, H. Koivisto3,
T. Thuillier4, J. W. Guo1, X. Z. Zhang1,2, H. Y. Zhao1,2, L. T. Sun1,2 and H. W. Zhao1,2
1Institute of Modern Physics (IMP), Chinese Academy of Sciences, Lanzhou 730000, China
2School of Nuclear Science and Technology, University of Chinese Academy of Sciences, Beijing 100049, China
3University of Jyväskylä, Department of Physics (JYFL), 40500 Jyväskylä, Finland
4Laboratoire de Physique Subatomique et de Cosmologie, 53 avenue des Martyrs, 38026 Grenoble Cedex, France
5STFC ISIS Pulsed Spallation Neutron and Muon Facility, Rutherford Appleton Laboratory, Harwell, OX110QX, UK

## Slide 2: Outline
Quick overview
Experimental setup
Investigation and results
Discussion and conclusion

## Slide 3: Quick overview
Correlation of magnetic field parameters to bremsstrahlung spectral temperature Ts
is not yet clear
Zhao H Y et al 2009 Plasma Sources Sci. Technol. 18 025021
Benitez J et al 2017 IEEE Trans. Plasma Sci. 45 1746–54
Possible correlation between bremsstrahlung spectra and the appearance of
electron cyclotron instabilities are still unknown
Tarvainen O et al 2016 Rev. Sci. Instrum. 87 02A703
minimum magnetic field Bmin and gradient at resonance zone ∇Becr are key parameters on Ts

## Slide 4: SECRAL-II ion source
Key parameters
GM cooler
He recondenser
LHe reservoir
Extraction
Plasma chamber
Solenoids
Sextupole
SECRAL-II
ωrf (GHz) | 18-28
Axial Field Peaks (T) | 3.7 (Inj.), 2.2 (Ext.)
Mirror Length (mm) | 420
No. of Axial SNs | 3
Br at Chamber Inner Wall (T) | 2.0
Magnet Cooling | LHe bathing
Chamber ID (mm) | 125.0
Dynamic cooling power (W) | ~6

## Slide 5: Bremsstrahlung detection system
Part 1
L:150mm ID:2.5mm OD:200mm
Pb collimator
Part 3
L:210mm ID:1mm OD:200mm
10mm diameter
extraction aperture
16mm diameter
puller aperture
X-ray blocking
2558.7mm
EXT
X-ray Blocking
Collimating System
Designed using MCNP code to avoid
  Thick target bremsstrahlung
  Secondary radiation
Part 2
L:300mm ID:20mm OD:220mm
SECRAL-II
Analyzing
magnet
XR-100-CdTe detector

## Slide 6: Spectral temperature Ts determination
I. Calibration applied
II. Spectra corrected for detector efficiency
III. Linear fit applied
Fitting range: 80-200 keV
Ts=-1/slope
In semi-log plot

## Slide 7: Microwave signal measurement system
0.01-26.5 GHz
Schottky Diode Detector
18GHz injection
24GHz injection

## Slide 8: Electron cyclotron instabilities
Γ is proportional to the anisotropy of the EVDF
Exponential growth of instability amplitude when Γ > Δ
Example of microwave signal associated with electron cyclotron instability on SECRAL-II
Driven by hot electrons interacting resonantly with electromagnetic plasma waves
A characteristic feature (independent on the mode) is emission of microwaves
Energy of microwave emission, Eµ, is described by growth and damping rates, Γ and Δ

## Slide 9: Source parameters
Beam | Xe
Frequency (GHz) | 18、24
Power (w) | 1500
Extraction Voltage (kV) | 20
Biased Disk Voltage (-V) | 40-50
Injection Pressure (mbar) | 1~2x10-7

## Slide 10: Experimental results- part 1 Constant Binj , Bext and Br while varying Bmin
Electron cyclotron instability
Note: on-axis ∇Becr is also changed when Bmin is changed
Binj: 1.75 T
Bext: 1.32 T
Br: 1.20 T
Bmin: 0.32-0.52 T
Bmin/Becr: 0.50-0.81
Binj: 2.60 T
Bext: 1.81 T
Br: 1.66 T
Bmin: 0.45-0.66 T
Bmin/Becr: 0.53-0.78

## Slide 11: Experimental results- part 2 Constant on-axis ∇Becr and Br while varying Bmin
Enlarged
Enlarged
Binj: 1.13-2.65 T
Bext: 1.03-1.68 T
Br: 1.02 T
Bmin: 0.31-0.47 T
Bmin/Becr: 0.48-0.73
on-axis ∇Becr ~6.3 T/m
Binj: 1.76-3.43 T
Bext: 1.45-2.05 T
Br: 1.44 T
Bmin: 0.39-0.57 T
Bmin/Becr: 0.46-0.67
on-axis ∇Becr ~9.2 T/m

## Slide 12: Experimental results- part 3 Constant Bmin and Br while varying on-axis ∇Becr
Binj: 1.06-2.41 T
Bext: 1.10-1.50 T
Br: 1.05 T
Bmin: 0.40 T
Binj: 2.12-3.58 T
Bext: 1.61-2.14 T
Br: 1.53 T
Bmin: 0.59 T

## Slide 13: Experimental results- part 4 Constant Binj , Bext and Bmin while varying Br
Binj: 3.00 T
Bext: 1.98 T
Bmin: 0.60 T

## Slide 14: Discussion -Correlation between Ts and electron cyclotron instabilities
Izotov I et al 2018 Plasma Sources Sci. Technol. 27 025012
Summary of Ts versus Bmin/Becr
Electron cyclotron instability

## Slide 15: Discussion -How to understand apparent linear Bmin dependence on Ts
Electron energy gain in single resonance crossing
Effective resonance width
depend strongly on ∇Becr
rather than Bmin
Average gradient over ECR surface：
Constant Binj , Bext and Br while varying Bmin
Constant on-axis ∇Becr and Br while varying Bmin

## Slide 16: Discussion -Plasma confinement
Br (T) | Bmin (T) | Binj (T) | Bext (T) | <∇Becr > (T/m)
1.05 | 0.40 | 1.06 | 1.10 | 6.92
 |  | 1.14 | 1.11 | 6.95
 |  | 1.16 | 1.12 | 6.98
 |  | 1.26 | 1.13 | 7.05
 |  | 1.49 | 1.21 | 7.13
 |  | 1.74 | 1.29 | 7.31
 |  | 1.98 | 1.37 | 7.43
 |  | 2.23 | 1.45 | 7.57
 |  | 2.41 | 1.50 | 7.70
Mirror ratio (Bmax/Bmin): 2.65-6.03
Constant Bmin and Br while varying on-axis ∇Becr

## Slide 17: Discussion -Plasma confinement
f (GHz) | Binj (T) | Bmin (T) | Bext (T) | Br (T) | <∇Becr > (T/m) | Blast (T)
24 | 3.00 | 0.60 | 1.98 | 1.35 | 9.09 | 1.05
 |  |  |  | 1.40 | 9.13 | 1.09
 |  |  |  | 1.44 | 9.18 | 1.13
 |  |  |  | 1.53 | 9.29 | 1.21
 |  |  |  | 1.62 | 9.39 | 1.29
 |  |  |  | 1.70 | 9.50 | 1.37
 |  |  |  | 1.78 | 9.61 | 1.45
Constant Binj , Bext and Bmin while varying Br
Weak effect of <∇Becr >
Blast defines overall magnetic confinement

## Slide 18: Conclusion
Bremsstrahlung spectral temperature Ts increases approximately linearly with the increase of Bmin/Becr up to ~ 0.8 and then saturates with the appearance of electron cyclotron instabilities, which suggests that periodic bursts of energetic electrons escaping the magnetic confinement will limit the increase of the energy content carried by the hot electron population and eventually lead to a saturation of Ts;
Increasing Bmin corresponds to decreasing <∇Becr > although the on-axis ∇Becr remains constant, which shows the inherent link between Bmin and <∇Becr > , and thus provides a viewpoint that is more coincident with theoretical studies to understand the apparent linear Bmin dependence and the appearance of electron cyclotron instabilities;
Ts decreases with the increasing of gradient (on-axis ∇Becr and <∇Becr>) at relatively low mirror ratio and is insensitive to the gradient at high mirror ratio when Bmin is constant, which indicates that Ts depends on not only electron heating, but also depends on electron confinement. This view is supported by the dependence of Ts on the radial confinement.

## Slide 19: Acknowledgement
J. Benitez, LBNL
D. Xie, LBNL

## Slide 20
Thanks for
your attention！

## Slide 21: Appendix
XR-100-CdTe Detector | 
Detector type | Cadmium Telluride (CdTe) Diode
Detector areas | 5 x 5 mm (25 mm2)
Detector thickness | 1 mm
Energy resolution @ 122 keV, 57Co | <1.5 keV FWHM, typical
Detector window | Be: 4 mil thick (100 µm)
Energy range | 10 – 300 keV
Detector efficiency | See below

## Slide 22: Appendix

## Slide 23: Appendix
Difference (with or without background subtraction) of TS is less than 0.16%
All data presented in this talk are spectra without background subtraction
Efficiency of Collimating System

## Slide 24: Appendix
The solenoid field model is constructed by fitting a sixth order polynomial Bz(z) to on axis magnetic field
The off-axis solenoid field is evaluated with a standard expansion
The sextupole field model is constructed by fitting a linear combination of cylindrical multipoles