## Slide 1: A Guiding Centre Approximation Approach for the Simulation of Electron Trajectories in ECR and Microwave Ion Sources
Antonio MENDEZ1, Thomas THUILLIER1, Tiberiu MINEA2
1Université Grenoble-Alpes, CNRS-IN2P3, Grenoble Institute of Engineering (INP), LPSC, 38000 Grenoble, France
2Université Paris-Saclay, CNRS-IN2P3, LPGP, 91405 Orsay, Île de France, France
ECRIS Workshop, Michigan, September 28th-30th 2020

## Slide 2: Introduction
Objective: Investigation of the validity and stability of the Guiding Centre (GC) algorithm to speed up particle propagation in magnetised plasma simulation.
2 ion sources to consider:
  ECRIS (Phoenix V2) confinement up to ~1ms.
  Microwave discharge (MDIS) ion source (SILHI@GANIL) confinement ~1µs.
Methodology:
  Implementation of two, otherwise identical, algorithms in c to simulate electron trajectories by Boris and the GC approximation.
  Consistency check and computation time measurement of trajectories for equivalent initial conditions with different time-steps (dt).
  Identify a range of validity for dt.
Notes: -I’m talking some more about these two ion sources later in this presentation

## Slide 3: Implementation
Boris Algorithm
GC initialization
Map (speeds up the computation per step without loss of accuracy)
For each electron:
  Compute magnetic moment
Number of electrons, maximum propagation time and time-step are given
Read provided magnetic field map files, merge them into a 3D grid.
Set electrons’ position () (uniform disc) and velocity () (Maxwell-Boltzmann)
Output
Track file (r, u, µ (GC), ne, ε, t, tcpu)
General initialization
GC Approximation
and integrated concurrently by RK4
Notes: -Magneto-static (low current, we keep the strong applied field constant)
-

## Slide 4: Boris algorithm
The standard for magnetised plasma simulations.
Second order, explicit method. Energy conserving while only a magnetic field is present.
For B= 1T, TB=1/ωB~35ps  dt~3ps.

## Slide 5: Guiding Centre (GC) approximation
Condition:
  The magnetic dipole moment (µ) is an adiabatic invariant if the motion along the plasma chamber is slow compared to the cyclotron motion .
  Equivalently, the Larmor radius should be much smaller than the length scale of B.

## Slide 6: Phoenix V2 ECRIS
Compact ECRIS commissioned for the SPIRAL 2 accelerator.
0.6L plasma chamber volume (L204mm , Ø63mm)
Operation frequency of 18GHz
Hexapole Br~1.35 T at wall
60 kV core
1.3-0.4-2.1 T Bz Axial Mirror

## Slide 7: Phoenix V2 min-B field
Map files provided to simulation
  2D for axisymmetric solenoidal fields
  3D for hexapolar fields
Figure: Phoenix V2 magnetic field and it’s gradient, longitudinal cross section map

## Slide 8: ECR orbit Far From Axis (FFA)
Good agreement between Boris and GC with ~1µs of propagation.
Figure: Confined electron orbit components
Figure: Confined electron orbit 3D plot
Z
X
X
Z
Y
x[cm]
y[cm]
z[cm]
time[µs]

## Slide 9: ECR orbit analysis (FFA)
GC algorithm ~20 times more computationally expensive per step.
  ~100 times larger timestep rends it faster.
The GC trajectories are stable up to a 100ps time-step, broken at a 1000ps.
Tboris = Boris computation time
Figure: Boris-GC orbit residual at corresponding propagation times.
24.5 TBoris
2.4 TBoris
0.2 TBoris
TBoris
Notes: 1 ev energy variation 1 turn
1 mus is typical for the electron free flight

## Slide 10: ECR orbit Close To Axis (CTA)
Figure: Confined electron orbit components
Figure: Confined electron orbit 3D plot
Disphasement observed between the GC and Boris orbits
Spatial envelopes are consistent.
Z
X
Y
Z
X
time[µs]
y[cm]
z[cm]
x[cm]

## Slide 11: ECR orbit analysis (CTA)
Figure: Boris-GC orbit residual at corresponding propagation times.
The observed disphasement is evident
Good agreement between Boris and GC
This orbit is one of the hardest for GC, (high axial oscillation frequency)
Stable at this time-scale
Energy conserved with both methods
Figure: Boris-GC orbit residual at corresponding propagation times.
Notes: Reasonably good energy conservation in the GC approach
Good spatial agreement between trajectories

## Slide 12: ECR confinement
Boris propagated e-
GC propagated e-
Good agreement for the confined electron distribution with both propagation methods
  Sample size 1000, largest valid dt (10-10s for GC and 10-12s for Boris)

## Slide 13: SILHI@GANIL ion source
2.45GHz operation frequency
Microwave discharge ion source (MW)
~0.1T maximum solenoidal magnetic field. (2D map given)
No magnetic confinement, one magnetic mirror towards extraction
Resonance surface
Gas
RF
Figure: SILHI source with permanent magnets (CEA/IRFU/GANIL)
Extraction wall
RF/Gas injection wall

## Slide 14: Trapped orbit in SILHI (one bounce)
Very good qualitative agreement.
A one bounce orbit chosen as it is one of the most challenging examples.
A typical energy electron of ~1eV is confined for ~1µs. In the absence of interaction
Figure: One bounce electron orbit components

## Slide 15: Trapped orbit analysis
Figure: Boris-GC orbit residual at corresponding propagation times.
GC algorithm ~5.7 times more computationally expensive per step.
10 times larger timestep rends it faster.
The GC trajectories stable up to a 1000ps time-step, broken at a 104ps.
  GC up to ~10 times faster when compared to Boris.
5.7 TBoris
2/3 TBoris
2/30 TBoris
Notes: Size of the field map
Mesh array size varies

## Slide 16: GC algorithm validity
ECRIS (Phoenix V2)
MDIS (SILHI)
The GC algorithm is more suitable for a MDIS (SILHI type) source than for an ECRIS
Figure: Validity condition for the GC algorithm for ECRIS and MDIS typical orbit

## Slide 17: Conclusions and prospects
The GC algorithm can accurately reproduce electron trajectories in the domain of both studied ion sources
  PHOENIX V2 ECRIS: B=1T, Te~1keV, volume=0.6L
  SILHI@GANIL: B=0.1T, Te~1eV, volume=0.6L
The GC algorithm can provide an advantage in terms of computation time for particle plasma simulations.
  This advantage is greater in a flat field, as observed for SILHI. The time step can be increased by a factor of 103 with a computation time two orders of magnitude smaller with respect to Boris.
  For the Phoenix V2 ECRIS the gains are more modest, with a time-step increased by a factor of 102 and one order of magnitude gain in computation time.
A smart switcher for orbit integration could be implemented, where the GC approximation is used with a large time-step when valid and a high time resolution isn’t required.

## Slide 18: References

## Slide 19: Appendix

## Slide 20: SILHI@GANIL B field and gradient

## Slide 21: Disphasement FFA

## Slide 22: GC approximation validity by electron’s kinetic energy
T [eV] | γ | v [m/s] | ~v⊥ [m/s] | B [T] | B [T/m] | ρ [µm] | B/B | (B/B)/ρ
1 | 1.000002 | 593097 | 342425 | 0.64 | 27 | 3 | 0.024 | 7792
10 | 1.000020 | 1875511 | 1082827 | 0.64 | 27 | 10 | 0.024 | 2464
100 | 1.000196 | 5930105 | 3423748 | 0.64 | 27 | 30 | 0.024 | 779
1,000 | 1.001957 | 18727914 | 10812566 | 0.64 | 27 | 96 | 0.024 | 246
10,000 | 1.019570 | 58455268 | 33749165 | 0.64 | 27 | 306 | 0.024 | 78
100,000 | 1.195695 | 164352596 | 94889016 | 0.64 | 27 | 1008 | 0.024 | 24
1,000,000 | 2.956955 | 282128500 | 162886965 | 0.64 | 27 | 4279 | 0.024 | 6
T [eV] | γ | v [m/s] | ~v⊥ [m/s] | B [T] |  | ρ [µm] |  | 
1 | 1.000002 | 593097 | 342425 | 0.64 | 27 | 3 | 0.024 | 7792
10 | 1.000020 | 1875511 | 1082827 | 0.64 | 27 | 10 | 0.024 | 2464
100 | 1.000196 | 5930105 | 3423748 | 0.64 | 27 | 30 | 0.024 | 779
1,000 | 1.001957 | 18727914 | 10812566 | 0.64 | 27 | 96 | 0.024 | 246
10,000 | 1.019570 | 58455268 | 33749165 | 0.64 | 27 | 306 | 0.024 | 78
100,000 | 1.195695 | 164352596 | 94889016 | 0.64 | 27 | 1008 | 0.024 | 24
1,000,000 | 2.956955 | 282128500 | 162886965 | 0.64 | 27 | 4279 | 0.024 | 6
Table: ECRIS near ECR region
T [eV] | γ | v [m/s] | ~v⊥ [m/s] | B [T] | B [T/m] | ρ [µm] | B/B | (B/B)/ρ
1 | 1.000002 | 593097 | 342425 | 0.102 | 0.3 | 19 | 0.340 | 17813
10 | 1.000020 | 1875511 | 1082827 | 0.102 | 0.3 | 60 | 0.340 | 5633
100 | 1.000196 | 5930105 | 3423748 | 0.102 | 0.3 | 191 | 0.340 | 1781
1,000 | 1.001957 | 18727914 | 10812566 | 0.102 | 0.3 | 604 | 0.340 | 563
10,000 | 1.019570 | 58455268 | 33749165 | 0.102 | 0.3 | 1918 | 0.340 | 177
100,000 | 1.195695 | 164352596 | 94889016 | 0.102 | 0.3 | 6324 | 0.340 | 54
1,000,000 | 2.956955 | 282128500 | 162886965 | 0.102 | 0.3 | 26848 | 0.340 | 13
T [eV] | γ | v [m/s] | ~v⊥ [m/s] | B [T] |  | ρ [µm] |  | 
1 | 1.000002 | 593097 | 342425 | 0.102 | 0.3 | 19 | 0.340 | 17813
10 | 1.000020 | 1875511 | 1082827 | 0.102 | 0.3 | 60 | 0.340 | 5633
100 | 1.000196 | 5930105 | 3423748 | 0.102 | 0.3 | 191 | 0.340 | 1781
1,000 | 1.001957 | 18727914 | 10812566 | 0.102 | 0.3 | 604 | 0.340 | 563
10,000 | 1.019570 | 58455268 | 33749165 | 0.102 | 0.3 | 1918 | 0.340 | 177
100,000 | 1.195695 | 164352596 | 94889016 | 0.102 | 0.3 | 6324 | 0.340 | 54
1,000,000 | 2.956955 | 282128500 | 162886965 | 0.102 | 0.3 | 26848 | 0.340 | 13
Table: MDIS near plasma chamber centre