## Slide 1: Conceptual design of an electrostatic trap for high intensity pulsed beam
W. Huang, L. T. Sun, Y. G. Liu, H. W. Zhao
University of Chinese Academy of Sciences, Institute of Modern Physics (IMP), Chinese Academy of Sciences (CAS)
D. Z. Xie
Lawrence Berkeley National Lab (LBNL), USA
2020/9/30 ECRIS 2020, East Lansing 1

## Slide 2
outline
Background
Principle of the ion trap
Design of the electron gun
Simulation of the ion trap
Summary
2020/9/30 ECRIS 2020, East Lansing 2

## Slide 3: background
 | HIAF/IMP | MEIC/JLab | FAIR/GSI | NICA/Dubna
Beam |  |  |  | 
I (emA) | 1.7 | 0.5 | 15 | 1.5
Ions/Pulse | 1xE11 | 2.5xE10 | 3.3E11 | 2E9
Pulse Width (µs) | 400 | 250 | 100 | 7
Frequency (Hz) | 1 | 5 | 1 | 50
Ion Source | ECR | ECR/EBIS | MeVVa (X) Now ECR | ESIS
Mode | AG | AG/Pulse | Pulse | Pulse
*AG: After Glow
Heavy ion beam requirements for the next generation accelerators
Arguments on ion beam compressor, LBNL, USA, 2016
2020/9/30 ECRIS 2020, East Lansing 3

## Slide 4: background
Present ECR performance on uranium beams in IMP
The requirement of HIAF for U34+ is 4 times of this performance.
4th generation ECR ion sources.
Ion trap.
Solutions
2020/9/30 ECRIS 2020, East Lansing 4
W. Lu et al., Rev. Sci. Instrum. 90, 113318 (2019).

## Slide 5: Principle of the ion trap
EBIS?
≤ 20% in the desired charge state distribution.
ECR?
Ions in CW mode
Accelerator
f=1 Hz, 10 ms
99% of the ions are wasted
Ion trap
Ions in CW mode
accumulation
Ion trap
Accelerator
Most of the ions are used.
More ions are in the desired charge state.
f=1 Hz
2020/9/30 ECRIS 2020, East Lansing 5

## Slide 6: Principle of the ion trap
An electrically confined ion beam compressor
Ub
Z
Gate
∆V(t-δ)
Vbunch(ƒ)
Trapping Section
L ~ 40 cm, Ø ~ 1.5 cm
Utrap
Bunching Section
L ~ 10 cm, Ø ~ 1.5 cm,
Bunching Efficiency ~ 0.5 - 0.6
∆E
~ 5 qeV
Arguments on ion beam compressor, LBNL, USA, 2016
2020/9/30 ECRIS 2020, East Lansing 6
ITRIP
*ITRIP: Ion Trap for high Intensity Pulsed beams

## Slide 7: Principle of the ion trap
features:
1. Extraction frequency ~ 1 Hz. (requirement of the HIAF)
2. No ionization of the desired charge state of ion.
3. Hollow structure of electron gun to extract the ions.
Design parameters | value
Length | 0.5 m
Magnetic field | ~ 0.5 T
Ee | < 1.2 keV (ionization threshold of U34+)
Ie | <1 A
Ion trapped (charges) | ~ 3E10
U34+ ions | ~ 1.5E10
e.g. U34+
2020/9/30 ECRIS 2020, East Lansing 7

## Slide 8: Design of the electron gun
Energy of electron ~ 1 keV, current ~ 440 mA.
Bmax ~ 5500 G
2020/9/30 ECRIS 2020, East Lansing 8
Cathode position
Radius=15 cm

## Slide 9: Design of the electron gun
Density distribution of electrons
r1 ~ 3 mm, r2 ~ 4.5 mm.
The depth of electron potential is ~ 0.3 kV.
2020/9/30 ECRIS 2020, East Lansing 9

## Slide 10: Simulation of the ion trap
Injection of ions
U34+
electrons
Electrons move back and forth.
2020/9/30 ECRIS 2020, East Lansing 10
Ions parameters:
radius ~5 mm, 0.1 emA
Energy of ions in the trap: (20 ~ 50) *q eV
*q: charge state
Reflecting electrode

## Slide 11: Simulation of the ion trap
U34+
Manipulation of potential
Ions can be trapped and accumulated in the trap.
potential (kV)
Drift tube
mm
m
Tracking without collisions.
2020/9/30 ECRIS 2020, East Lansing 11
electrons

## Slide 12: Simulation of the ion trap
Accumulation of electrons
Accumulation of ions
After 1 s:
Capacity:
5.0E12 electrons ~ 1.4E11 U34+
In the trap
3.4E10 U34+
50% extraction efficiency
1.7E10 ions/pulse
Without collisions
Intensity
2020/9/30 ECRIS 2020, East Lansing 12

## Slide 13: Simulation of the ion trap
Evolution of charge state of ions
Parameters: accumulation of U34+ ions as fitting curve, vacuum 1E-10 Torr,
electron current is 440 mA with an energy of 1 keV.
Considering only charge exchange and radiative recombination processes.
After 1 s:
In the trap
1.24E10 U34+
50% extraction efficiency
6.2E9 ions/pulse
Intensity
2020/9/30 ECRIS 2020, East Lansing 13
Need more effort!

## Slide 14
summary
An ion trap based on ECRIS is proposed for high intensity highly charged ions.
The ion trap is a promising and economic device.
The above discussed design can be further refined for better efficiency but should be verified with experiments.
Thank you for your attention!
2020/9/30 ECRIS 2020, East Lansing 14