## Slide 1
Numerical Simulations of Plasma Dynamics in ECRIS Afterglow
Li Lei1, Xiaolin Jin1*, Jibo Li2, Tao Huang1, Zhonghai Yang1 and Bin Li1
Vacuum Electronics National Laboratory, University of Electronic Science and Technology of China, Chengdu
Institute of Modern Physics, Chinese Academy of Sciences, Lanzhou
Email address: jinxiaolin@uestc.edu.cn
24th International Workshop on ECR Ion Source (ECRIS’20)
28-30th, September, 2020

## Slide 2
ECRIS Set-up
Cavity Radius | 19 mm
Cavity Length | 78 mm
Aperture Radius | 6 mm
MW Mode | TE1,1
MW Frequency | 14.5 GHz
MW Power | 500 W
ECR Magnetic Field | 0.518 T
Plasma Species | Argon
Plasma Density | 1012 cm-3
Critical Parameters
Layout of LAPECR1U
extraction
aperture
ECR zone

## Slide 3
Simulation Scheme
Energetic Electrons
Single Particle Simulation
Electrons (~10 eV) uniformly distributed at first
Coulomb Collision is considered with constant scattering factor
Rejoin system as new particles when out of bounds
Electrons are heated till average energy reaches 10 keV
Distributions of the electrons are sent to the 2nd step as initiation
ECRIS Operation
Implicit Particle-in-cell Simulation
Cold Electrons (~10 eV) uniformly distributed at first
Ions (~1 eV) distributed due to quasi-neutrality
Coulomb Collision is considered with computed local plasma density
Secondary emission for electrons and absorption for ions when out of bounds
Ionization is omitted, and in stead new particles are manually created
Two-Step Simulation for A Stable Operation

## Slide 4
Without
MW Power
MW power is critical to the formation of the potential dip.
ECRIS Potential at CW Operation
With
MW Power
Energetic electrons (well-confined)
as backgrounds instead of being tracked

## Slide 5
Density Distribution
Power Off
assuming that the energetic electron distribution still remain unchanged
Cold electrons by itself may not contribute much to the ECRIS afterglow.
Cold Electrons at Power-off

## Slide 6
Energetic Electrons at Power-off
Density Distribution
Power Off
Single particle simulation
Energetic electrons are less confined at power-on due to RF diffusion.

## Slide 7
Summary
Next Works:
Track energetic electrons in the simulation once an appropriate velocity distribution has been calculated.
Consider multi charge state ions and step-wise ionization.
Extend simulation time for diagnostics of ion dynamics.

## Slide 8
Thanks for your attention!