## Slide 1
Present status of HIMAC ECR ion sources
HIMAC
NIRS
M. Muramatsu1, K. Takahashi2, T. Suzuki2, F. Ouchi2,
S. Hashizaki2, M. Sei2, T. Sasano2, T. Shiraishi2, T. Kondo2,
M. Kawashima2, Y. Iwata1, and A. Kitagawa1
1 National Institutes for Quantum Radiological Science and Technology (QST-NIRS), Japan
2 Accelerator Engineering Corporation (AEC), Japan

## Slide 2: Heavy Ion Medical Accelerator in Chiba (HIMAC)
NIRS-HEC
Kei2
NIRS-PIG
RFQ Linac
(800keV/n)
Alvarez Linac
(6MeV/n)
Upper Synchrotron
(800MeV/n)
Lower Synchrotron
(800MeV/n)
Therapy room
Biology
Exp. room
High-Energy
Beam-Transport Line
Operation room
Specifications
-Ion species He-Si
-Max. energy 800 MeV/n
-Size 70 m(W), 120 m(L), 30 m(H)
NIRS-ECR
Kei3
Notes: 2

## Slide 3: Patient Enrolled in Carbon Ion Therapy at QST (June 1994～ March 2020)

## Slide 4: 10 GHz NIRS-ECR ion source
  - TWT Amp., 9.75-10.25 GHz, 1 kW
  - Mirror field: 0.93 T / 0.76 T
  - Axial field: 0.8 T
  - Extraction voltage: 25kV max.
  - C4+: 430 mA (C2+: 200 mA for therapy)
  Production of C2+ ion for medical use

## Slide 5: 18 GHz NIRS-HEC source
Mirror coil
TMP
High voltage
TMP
Einzel
TMP
FC
KLY: 18 GHz, 1400 W
TWTA: 17.10 – 18.55, 1200 W
Extraction voltage : 60 kV max.
  Production of heavy ions (Ar, Fe, Kr, Xe)
  for biological and physical experiment

## Slide 6: Prototype ion source for carbon ion radiotherapy (Kei2-source)
  Production of C4+ ion for biological experiment in HIMAC
  All permanent magnet
    Mirror field: 0.84 T / 0.55 T
    Radial field: 0.75 T
  Extraction voltage: 30 kV max.
  Commercial model (Kei series):Gunma, Saga, Kanagawa, Osaka, Yamagata -> under operating

## Slide 7: Prototype ion source for various ion production (Kei3-source)
  Development of ECR ion source (two frequency heating, gas mixing…)
  All permanent magnet
    Mirror field: 0.84 T / 0.55 T
    Radial field: 0.75 T
  Extraction voltage: 30 kV max.

## Slide 8: Operation of ion sources at HIMAC in 2019
49.7%
25.7%
14.1%
10.4%
  Operation time of various ion species in 2019
  ECR: 10 GHz NIRS-ECR, HEC: 18 GHz NIRS-HEC
  PIG: NIRS-PIG, KIS: 10 GHz Kei2-source
- Total operation time of ion sources were 9786.16hour in 2019.
- ECR produce C ion for medical use,
- HEC: Heavy ion, isotopic gas, PIG: light ion, spattering, KIS: carbon, He
- Operation time of carbon was 5923.04 hour (ECR: med., KIS, HEC, PIG: exp.)
  Ratio of operation time and ion species in 2019

## Slide 9: Operation time of HIMAC synchrotron
Upper synchrotron ring
- Carbon for medical use and few bio. Phys. experiment
- Beam energy for medical use is 56-430 MeV/n
- Other ion used for biological and physical experiment
Lower synchrotron ring
- Biological and physical experiment
- Iron and Oxygen are used a lot next to carbon

## Slide 10: Development of 18 GHz NIRS-HEC
Gas switching at NIRS-HEC for multi-ion irradiation
- pulsed gas by solenoid valve
- production of He+, C2+, O3+, Ne4+
- beam switching
Production of Indium and Tin ion at 18 GHz NIRS-HEC
- In: In(C5H5)
- Sn: Sn(i-C3H7)4

## Slide 11
T. Inaniwa et al., Physics in Medicine and Biology, 62, p.5180 (2017).
Multi-ion irradiation: Optimization of ion species by irradiation area
  Center of tumor: Neon, Oxygen (higher biological effect than carbon)
  -> Suppression of cancer recurrence
  Around the center of the tumor: Carbon
  Near normal tissue: Helium (lower biological effect than carbon)
  -> Reducing side effects
Multi-ion irradiation
C
He
O
Dose distribution with He, C, O at pancreas
Distribution of LET with He, C, O at pancreas
Irradiation area
C
He
O
Center of tumor
Ion source: production of He, C, O, and Ne ion

## Slide 12: Gas switching system
Material for ion production
He: He2+
CO2: C2+, O3+
Ne: Ne4+
CO2
He
Ne
NIRS-HEC
Solenoid valve

## Slide 13: Gas switching system
Material for ion production
He: He2+
CO2: C2+, O3+
Ne: Ne4+
He
Ne
NIRS-HEC

## Slide 14: Exhaust time of gases
 | Pulse width [msec] | Repetition [Hz] | Pressure [MPa] | Time to 1.0E-5 Pa [sec]
He | 0.12 | 1.2 | 0.00 | 5
CO2 | 0.3 | 1.2 | -0.05 | 11
Ne | 0.25 | 1.2 | 0.00 | 7
27 sec
42 sec
51 sec

## Slide 15: Beam switching time

## Slide 16: Development of ECRIS
Gas switching at NIRS-HEC for multi-ion irradiation
- pulsed gas by solenoid valve
- production of He+, C2+, O3+, Ne4+
- beam switching
Production of Indium and Tin ion at NIRS-HEC
- In: In(C5H5)
- Sn: Sn(i-C3H7)4

## Slide 17: Production of Indium and Tin ion
Peltier cooler for MIVOC
0-room temperature
W. Takasugi RSI 81, 02A329 (2010)
Material
In: In(C5H5)
Sn: Sn(i-C3H7)4

## Slide 18: Production of Is ion from In(C5H5)
DEVICE | UNIT | PRESET | 
TG1_D | msec | 152.39 | 
TG1_W | msec | 12 | 
TG2_D | msec | 152.4 | 
TG2_W | msec | 11.9 | 
M_GFL | cc/min | 0.08 | O2
S_GFL | cc/min | 0 | 
AMP1:F | W | 1200 | 
AMP2:F | W | 600 | 
LENS_D | kV | 7.2 | 
MRR1 | A | 865 | 
MRR2 | A | 570 | 
EXT_D | kV | 31 | 
AG_D | kV | 46 | 
BD | V | 100 | 
TEMP | Degree C | 6.2 | 
BA | mT | 187.48 | 
SLTA02 | mm | 10 | 
SELF | sec | 0.412 | 
Optimized for 20+
115In20+: 90 mA
Beam current [mA]
Magnetic field [mT]

## Slide 19: Production of Sn ion from Sn(i-C3H7)4
DEVICE | UNIT | PRESET | 
TG1_D | msec | 0 | 
TG1_W | msec | 75 | 
TG2_D | msec | 0 | 
TG2_W | msec | 75 | 
M_GFL | cc/min | 0 | O2
S_GFL | cc/min | - | 
AMP1:F | W | 950 | 
AMP2:F | W | 200 | 
LENS_D | kV | 6 | 
MRR1 | A | 865 | 
MRR2 | A | 550 | 
EXT_D | kV | 32 | 
AG_D | kV | 53.333 | 
BD | V | 100 | 
TEMP | Degree C | 9.2 | 
BA | mT | 215.71 | 
SLTA02 | mm | 5 | 
SELF | sec | 0.412 | 
Optimized for 18+
120Sn18+: 15 mA
not separation
Beam current [mA]
Magnetic field [mT]

## Slide 20: Conclusion
Operation in 2019
- Total operation time: 9786hour
- Without big trouble (discharge, operation mistake)
Development of ECRIS
- Gas switching at NIRS-HEC for multi-ion irradiation
- production of He+, C2+, O3+, Ne4+
- switching time: 7-35 sec
- Production of Indium and Tin ion at NIRS-HEC
- 115In20+: 90 mA
- 120Sn18+: 15 mA (?)

## Slide 21: Thank you

## Slide 22: Heavy ion radiotherapy facilities worldwide